## Slide 1: Removal of Motion Artifacts from Photoplethysmogram Data for Feature Based Diagnosis of Atrial Fibrillation
By: Supervisor:
Salaar Ali Assad - 21100087 Dr. Muhammad Tahir
Sheraz Hassan - 21100285
Mohammad Afaq - 21100214
Department of Electrical Engineering
Lahore University of Management Sciences

## Slide 2: Removal of Motion Artifacts from Photoplethysmogram
for Feature Based Diagnosis of Atrial Fibrillation

## Slide 3: Motivation
19% of the Pakistani population suffers from Cardiovascular Diseases (CVDs), making it the leading non-communicable disease in the country [1]
Increasing demand for Electrocardiogram (ECG) which are uncomfortable, expensive, limited and require medical supervision [2]
Wrist worn photoplethysmogram (PPG) devices offer a simpler, cheaper and more comfortable alternative

## Slide 4: Vision
Allow for remote and ambulatory cardiac health monitoring and assessment
Identification and removal of artifacts from the PPG data
Develop data processing algorithm for a robust diagnosis of cardiac disorders

## Slide 5: Block Diagram

## Slide 6: Background Review

## Slide 7: PPG Waveform
Important terms
Systolic Phase
Diastolic Phase
Pulse Wave Duration
Blood Volume Pulse (BVP)
PPG Waveform Notation [3]

## Slide 8: Perfusion Effect
Variation of blood flow volume in capillary network and the surrounding tissue
Causes a baseline shift in the raw PPG signal.
Factors
Breathing rate
Activity
Anxiety
Stress
And much more!
PPG Signal without perfusion (top) and with perfusion (bottom) [4]

## Slide 9: Motion Artifact
Healthy Patient with No Motion Artifacts
Disturbance in the contact between the skin and sensor from movement of the body
Introduces noise into the readings making them unreliable and inaccurate
Readings cannot detect Atrial Fibrillation (Afib) reliably

## Slide 10
Patient with Afib
Corrupted Signal with Motion Artifacts

## Slide 11: Methodology

## Slide 12: High-End Device
Empatica E4
4 LED’s and 2 photodiodes
PPG sensor (64HZ)
3-axis accelerometer (32Hz)
Temperature sensor
Pre-processing algorithm
Front and Back View of the Empatica E4

## Slide 13: Low-End Device
Maxim MAXREFDES103#
2 LED’s and 2 photodiodes
IR emitter
Variable sampling rate
Front and Back View of the Maxim MAXREFDES103

## Slide 14: Cost Analysis
 | Description | Qty | Unit Price (USD $) | Total price (USD $)
1- | Empatica E4 wristband | 1 | 1690 | 1690
2- | MAXREFDES103#: Health Sensor band | 3 | 199 | 597

## Slide 15: Software
MATLAB
MATLAB is being used majorly for signal processing and analysis.
Jupyter Notebook
We used Jupyter notebook environment for all our python-based working.
Maxim UI/ Empatica UI
UI of Empatica was very straight forward to interact with whereas UI of Maxima required some understanding

## Slide 16: Data sets
Three different types of data sets were used
Pre-existing data sets of 46 individuals
Data sets collected under homogenous environment using both E4 and Maxim.
Data sets from the IEEE signaling cup

## Slide 17: Data Quality Comparison - Maxim
17
Green least prone to motion artifacts
Red and IR as reference

## Slide 18: Data Quality Comparison - Maxim
Average Sampling rate =
18
Sampling rate/Hz | Sampling average | Averaged sampling rate/Hz
64 | 1 | 64
128 | 2 | 64
256 | 4 | 64
512 | 8 | 64
1024 | 16 | 64

## Slide 20
20
MAXREFDES103 Signal = Perfusion waveform + PPG waveform + noise (2)
E4 Signal = PPG waveform + noise (1)
Low-end vs High-end

## Slide 21: System level design of Raw PPG data
Raw PPG data contains 3 types of artifacts
Motion
Perfusion
Noise

## Slide 22: Separating Perfusion and PPG Waveform from Raw PPG Signal

## Slide 23: Approximate Perfusion Waveform using a Polynomial

## Slide 24: Approximate Perfusion
Savitzky-Golay Filter
Filtering of noise and smoothing of signal
order polynomial
Frame Length

## Slide 25
Raw PPG Signal (Blue) along with the approximated Perfusion Waveform (Red)
PPG Waveform obtained along with its Frequency Plot

## Slide 26: Filter out PPG Waveform

## Slide 27
Raw PPG signal and its frequency plot from MAXREFDES103
PPG waveform and Perfusion waveform obtained by filtering using a band pass filter

## Slide 28: Parameter Estimation

## Slide 29: Breath Rate
Respiratory signal dominated by frequencies at 0.3 Hz
Apply band pass filter
Find Peaks
Average of distance between successive peaks in samples

## Slide 30: Motion Artifacts Removal

## Slide 31: Accelerometer correlation?

## Slide 32
Analysis
1) Individual at rest
  Reference signal

## Slide 33
BVP of a healthy individual with motion along with its magnitude spectrum using the E4
2) Individual with a controlled vertical motion

## Slide 34
Filtered BVP using frequency of motion in the accelerometer data of E4 (A) Before (B) After
  Apply Filter :
  Band stop filter: FIR Equiripple with order 100 and bandwidth [5]
(A)
(B)

## Slide 35
Repeated with MAXREFDES103
Comparison of inverted PPG waveform before and after eliminating frequencies of motion using MAXREFDES103

## Slide 36: Conclusion
Correlation do exist
Motion artifacts removed to some extent
Noise frequencies > 0.5 Hz cannot be filtered without having the risk of losing vital PPG information

## Slide 37: Future Work
Motion Artifact Removal
  Explore and implement other algorithms
Health Parameter Approximation from Perfusion
  Extract and analyze feature parameters
Expand our Dataset
  Diversify across age and gender

## Slide 38: Thank You!
Any Questions?

## Slide 39: References:
[1] S. Naseem, U. K. Khattak, H. Ghazanfar, and A. Irfan, \Prevalence of noncommunicable diseases and their risk factors at a semi-urban community, Pakistan," Pan Afr Med J, vol. 23, p. 151, 2016.
[2] S. Lee, G. Ha, D. Wright, Y. Ma, E. Sen-Gupta, N. Haubrich, P. Branche, W. Li, G. Huppert, M. Johnson, B. Mutlu, K. Li, N. Sheth, J. Wright, y.-s. Huang, M. Mansour, J. Rogers, and R. Ghaari, \Highly exible, wearable, and disposable cardiac biosensors for remote and ambulatory monitoring,“ npj Digital Medicine, vol. 1, 12 2018.
[3] C. Fischer, M. Glos, T. Penzel, and I. Fietze, \Extended algorithm for realtime pulse waveform segmentation and artifact detection in photoplethysmograms,“ Somnologie, vol. 21, pp. 1-11, 05 2017.
[4] Charlton P.H., Villarroel M., Salguiero F. (2016) Waveform Analysis to Estimate Respiratory Rate. In: Secondary Analysis of Electronic Health Records. Springer, Cham. https://doi.org/10.1007/978-3-319-43742-2_26
[5]S. Nabavi and S. Bhadra, ”A robust fusion method for motion artifacts reduction in photoplethysmography signal," IEEE Transactions on Instrumentation and Measurement, vol. PP, pp. 1-1, 07 2020.